## Slide 1: COMBIVIS connect „Remote Maintenance“
Workshop ISM 2015
Zacharewicz / Meyer
V1.1_EN

## Slide 2: Topics
1. Softwarearchitecture
2. COMBIVIS connect Domain / Control Center
3. COMBIVIS connect Runtime
4. General functions of COMBIVIS connect
7. Network security (Firewall)
5. User- and device management
6. VPN connection / serial connection
8. Network bridge / subnetwork

## Slide 3: Software architecture
Topic

## Slide 4: Software architecture (C6 Router)
COMBIVIS Control Center: Software application on the office PC
COMBIVIS Connect Runtime: Software componente on the remote PC/HMI
COMBIVIS Connect Cloud: distributed support infrastructure
COMBIVIS connect Control Center

## Slide 5: COMBIVIS connect Control Center / Domain
Topic

## Slide 6: Activate connect domain
One-time, a license fee will be charged for the registration of the domain
With your order you will receive an USB key with the COMBIVIS connect software
Registration of COMBIVIS connect Domain

## Slide 7: Run setup from USB KEY
Now run the setup from USB key
Hinweis:
An installation and use of the COMBIVIS connect Control Center software is allowed on several local PCs
A virtual network adapter and a virtual serial port are added on the local PC during the installation  it is necessary for the VPN via Ethernet or serial connection
Notes: Installations- Datei vom COMBIVIS Control Center
Die COMBIVIS Control Center Software kann auf mehrere lokale PCs installiert und genutzt werden, um eine Verbindung zu den Remote-Geräten herzustellen.
Ein virtueller Netzwerkadapter und eine virtuelle serielle Schnittstelle werden während der Installation den bereits vorhandenen Netzwerkadaptern des Remote-Gerätes hinzugefügt.
Sobald eine VPN-Verbindung aufgebaut wird, wird dem virtuellen Adapter des lokalen PCs automatisch eine freie IP-Adresse zugewiesen. Diese IP-Adresse befindet sich im gleichen Adressbereich des virtuellen Adapters oder der Netzwerkbrücke des Remote-PCs.

## Slide 8: Create your domain 1/2
Create a new domain

## Slide 9: Create your domain 2/2
Fill in the domain properties

## Slide 10: Request domain license 1/2
After filling in the domain properties, the domain must be requested (request is automatically sent)

## Slide 11: Request domain license 2/2
Recieve an email with the admin account details
Benutzername
Domain
Passwort

## Slide 12: Run unlimited activation key 1/4
Log in with the forwarded admin account

## Slide 13: Run unlimited activation key 2/4
Now, the domain must be activated
Change to the „Domain Account“ view

## Slide 14: Run unlimited activation key 3/4
Register the domain

## Slide 15: Run unlimited activation key 4/4
Enter the license serial number from nameplate of USB key box
After registration, the domain process is done

## Slide 16: COMBIVIS connect Runtime
Topic

## Slide 17: Licensing COMBIVIS connect runtime
To allow the remote access to the remote PCs/HMIs, the COMBIVIS connect runtime must be started
Push the button "Connect" to establish the connection to the server infrastructure
Inform the COMBIVIS connect administrator about the ID and the password

## Slide 18: Add device to domain 1/3
Administrator or authorized users add remote PC/HMI in the corresponding folder of the domain
Administrator assigns permissions to selected users

## Slide 19: Add device to domain 2/3
The COMBIVIS connect runtime must be registered using the license number of device nameplate (PC/HMI)

## Slide 20: Add device to domain 3/3
Now, the device (PC/HMI) was added to your domain

## Slide 21: COMBIVIS connect Runtime
Identification of the different operation modes
You can find the icon in the taskbar
Notes: It gives different operation modes of the COMBIVIS connect Runtime:
Icon grey:
  The remote device is disconnected from the COMBIVIS connect network.
Icon pink:
  The remote device is connected to the COMBIVIS connect network but no user has connected with this device.
Icon green:
  The remote device is connected to the COMBIVIS connect network and one or more users have connected with this device.

## Slide 22: General Functions of COMBIVIS connect
Topic

## Slide 23: Connection with server infrastructure 1/2
Start COMBIVIS connect runtime and connect the remote PC to the server
Start COMBIVIS connect Control center  connect the local PC with the server after entering of domain, user name and password

## Slide 24: Connection with server infrastructure 2/2
Remote devices which are currently connected to the server are displayed under the register "Device“ (green marked)

## Slide 25: Network settings 1/3 (Proxy)
Proxy possibilities:
  Auto: Use Internet-Explorer settings (IP address and port) (without user name and password)
  HTTP, SOCKS5: Support authentication with user name and password
  None: No Proxy is used for the connection

## Slide 26: Network settings 2/3 (Port)
Port options for the connection between Control Center and infrastructure
  Auto: Use the first available port (TCP or UDP) 443, 80, 5935.
  80, 443, 5935: Use the adjusted port

## Slide 27: Network settings (Connectifity) 3/3
Peer-To-Peer connection options between Control Center and CV connect Runtime
  Auto: If possible, the P2P is used to connect to the destination Runtime, otherwise the mirror server will used.
  Disabled: Uses the connection via the mirror server without an attempt via P2P approach.

## Slide 28: Log file of the server connection
The user can receive all important information about the intended connection in the Log file.
The Log-file consists the date, the time and the current status of the connection.

## Slide 29: Remote desktop
Start the CVS Connect Runtime / CVS Connect Control Center and connect with the server infrastructure
Choose the corresponding remote PC/HMI
Call up the desktop of the remote PC/HMI about the „Remote Desktop“- button on your local PC  remote control of the remote PC/HMI

## Slide 30: Remote explorer
Choose the function „Remote Explorer“
Enables the
  creating folders as well as the deleting and renaming of folders and files
  file exchange between local PC and remote PC  similar to Windows Explorer

## Slide 31: Statistics and reports
Under the function statistics and reports, the administrator receives the following information:
  which user logs in
  on which remote PC the user has logged in
  at what time has a user logged in or logged out
  how long was the user logged in
Notes: Protocols of connection
  Server-Infrastruktur keeps a minutes (protocol) about all connections which were made on a certain domain.
  The information is available to the domain administrator for the check and supervision.

## Slide 32: Chat
Enables the written conversation with the user at the remote PC
Messages are sent to the desktop of the remote PC  User of the remote PC can reply about real keyboard or software keyboard

## Slide 33: Further functions
Reboot  Reboot the remote PC (COMBIVIS Connect Runtime starts automatically)
Remote Process-Manager  Process management (similar to Windows process management)
System-Information  Device name, Computer name, Version of operating system, IP addresses, etc.
1
2
1
2

## Slide 34: User- and Device-Management
Topic

## Slide 35: User management 1/5
Only the administrator has the access to the user management and he can
  add, edit and delete the corresponding users
  allocate an initial password for the new user
  add new user groups and assign corresponding users to them
Groups/Users can be assigned the folders and the devices within the folder inherits these permissions

## Slide 36: User management 2/5
Group/User permissions can be also assigned directly to the devices
Rules which were assigned to sub-folders or devices, cancel higher folder rules
Permissions can be changed for certain user of a group, even if the user belongs to a group with other permissions

## Slide 37: User management 3/5
Allocation of permissions for groups/users in the form of profiles
The defined access rules always refer to a folder or device

## Slide 38: User management 4/5
To assign permissions, the following procedures have to be executed:
  Choice of the folder or device
  Allocation of group/user to a folder or a selected device

## Slide 39: User management 5/5
    Allocation of the profiles to every group/user who is assigned to the folder or device

## Slide 40: Device management 1/2
After a device was added to the domain or to the folder using its ID and password, it can be
  assigned to a available folder or a new folder
  unlocked by entering the requested license key

## Slide 41: Device management 2/2
The folders can be assigned several users or user groups
All users can be allowed or denied specified permissions

## Slide 42: VPN connection / Serial connection
Topic

## Slide 43: VPN connection 1/7
VPN = virtual private network on a public infrastructure
only communication partners who belong to the network can communicate and exchange data with each other
the COMBIVIS connect server infrastructure corresponds to highest safety standards  SSL / TLS protocol
therefore, the connection is access- and manipulation-proof (Protection against attacks such as „Man in the middle attack, Brute force attack, Password theft …)
VPN-partners can establish a connection through an insecure network, without an increased risk
enables the KEB device search with COMBIVIS 6 via Ethernet

## Slide 44: VPN connection 2/7
Notes: COMBIVIS Control Center authenticates based on domain name, user name and password.
The COMBIVIS connect Server Infrastructure enables the Control Center user to connect to the remote Runtime system registered in the domain.
The COMBIVIS connect Runtime authenticates with COMBIVIS connect Server Infrastructure using a unique certificate
After the Runtime component is connected and authenticated, the Control Center can initiate an end-to-end secure connection. When a direct peer-to-peer connection is not possible, the connection can be forwarded by the server infrastructure.
Control Center and Runtime connect to the COMBIVIS connect Server Infrastructure using a secure connection (SSL/TLS)
  The outgoing connection is recognized safe and approved by means of firewall rules
  Usable ports are: 80, 443, 5935
  If UDP ports are available, these should be used to improve the performance
Messages are not decoded by COMBIVIS Connect Cloud because the SSL connection "end-to-end" is secured.

## Slide 45: VPN connection 3/7
Start the Connect Runtime / Connect Control Center and connect the Server
Choose the desired remote PC and open the VPN-window via VPN button

## Slide 46: VPN connection 4/7
Start the VPN connection via the button "connect”

## Slide 47: VPN connection 5/7
After successful connection, the connection is displayed in magenta
Remote PC has the IP-address 10.8.01 (virtual interface)  automatically assigned during the COMBIVIS connect runtime installation
Control Center PC receives a free IP-address (e.g. 10.8.0.2) in the same IP-area

## Slide 48: VPN connection 6/7
Display of connection quality for
  Local network
  Remote network (Subnetwork)

## Slide 49: VPN-connection 7/7
Communication protocol options of the VPN-connection
  Auto: If it is not blocked for other reasons, the use of the UDP protocol is prefered for VPN connection, otherwise the TCP protocol is used
  Force TCP: Use the TCP protocol for the VPN connection
UDP packets may be filtered or penalised in some network infrastructures (e.g. Firewall).
Set the parameter schown above to „Force TCP“.

## Slide 50: Serial Passthrough 1/4
on local PC, a virtual serial interface for the serial passthrough mode was established during the installation of COMBIVIS connect Control Center
serial remote access to remote devices through the physical serial port of the remote PC  COM interface is selectable
serial communication is possible via RS232 or RS485 (RS485 at the C6-IPC is only possible in conjunction of a converter)
supports the passage of the serial data stream to remote serial device interface both as half- as well as full-duplex connection
enables the KEB device search with COMBIVIS 6 via Ethernet

## Slide 51: Serial Passthrough 2/4
Start the Connect Runtime / Connect Control Center and connect the Server
Establish a VPN connection between local PC and remote PC
Call up the serial passthrough mode via "Serial" function

## Slide 52: Serial Passthrough 3/4
Select the physical serial interface of the remote PC
The virtual COM-Port number of the local PC is entered by the user during the installation of COMBIVIS connect
Activate the serial data communication via the VPN tunnel with the button “connect”

## Slide 53: Serial Passthrough 4/4
There are three different setting possibilities for data transfer, interface configuration and handshake signals:
    Data only:
      This setting transmits only data.
      It requires the manual setting of the serial communication interface parameters.
    Data + Port configuration: (easiest setting)
      This setting transmits data and serial interface configuration.
      The serial interface will be automatically configured by the system.
    Data + Port configuration + Data signals:
      This setting transmits data, serial interface configuration and control signals.
Some serial protocols of automation devices are very sensitive to latency, and the remote serial communication could not work, even in the presence of very good connection times.

## Slide 54: Firewall
Topic

## Slide 55: Firewall - General
Integrated Firewall makes definition and application of rules possible for the
  dertermination other security levels
  limitation of the data traffic on the VPN channel
The configuration method corresponds the procedure at conventional firewall systems
The addition of policies (guidelines) takes place about the both upper Firewall icons

## Slide 56: Firewall – Import of policies (guidelines)
By clicking the import icon , a list of available policies is shown
Confirm the selection of the desired policy by clicking the "OK" button
The policy is inserted in the folder structure in dependent on the selected folder

## Slide 57: Firewall – Personalised definition of policies 1/3
Mark a folder in which the policy is created
Then click on the button to define the rule
Give the policy a name

## Slide 58: Firewall – Personalised definition of policies 2/3
By addition, a rule is inserted in the definition of the policy
The VPN of COMBIVIS connect supports the virtualisation of the datalink level whereby the integrated firewall enables the definition of policies
The list „Ethernet-Type“ is a collection of all usual protocols which are used on Ethernet level

## Slide 59: Firewall – Personalised definition of policies 3/3
If "IP" is selected as an Ethernet type, the included IP address, the IP protocol and the IP port must be specified
With every step, the window „Firewall“ dynamically adapts itself on basis of the made selection

## Slide 60: Firewall – Applying the policies (guidelines) 1/6
Usage of the defined policies takes place on folder level but also at the level of individual devices
The policies / rules, which should be accordingly applied, can be added to the area "firewall"

## Slide 61: Firewall – Applying the policies (guidelines) 2/6
The default action for the domain is set to „Allow“ at the beginning
If no firewall policies / rules have been added, so all data packets are passed through without verification

## Slide 62: Firewall – Applying the policies (guidelines) 3/6
There is a difference in the definition of policies between
  negative logic  default action = Allow / policy = Deny
  positive logic  default action = Deny / policy = Allow
negative Logik
positive Logik
Bezug auf Aktion der Richtlinien
Bezug auf Aktion der Richtlinien

## Slide 63: Firewall – Applying the policies (guidelines) 4/6
Negative logic  only the denied packages by the policy are blocked
  Setting the Default action on "Allow”
  Set the action within the policy on “Deny”

## Slide 64: Firewall – Applying the policies (guidelines) 5/6
Positive logic  only the allowed packages by the policy are passed through
  Setting the Default action on “Deny”
  Set the action within the policy on “Allow”

## Slide 65: Firewall – Applying the policies (guidelines) 6/6
Applied policies can be inherited on subfolders and its contained devices.
If the inheritance chain is not interrupted (CheckBox not marked), the default action is specified by a higher-level folder
The Firewall area is always a summary of both inherited and explicitly applied policies for each selected device or folder
“Standardaktion” vom übergeordneten Ordner vererbt
“Standardaktion” nicht vom übergeordneten Ordner vererbt

## Slide 66: Firewall – Example to the protocol filter 1/2
Import a pre-defined policy and their usage for a device  independent of the user and the IP address of this device
  Select a domain and then click the "Import Policy" button
  Mark the desired policy in the list and import this with "OK“
  Afterwards, select the device to which the policy shall be applied

## Slide 67: Firewall – Example to the protocol filter 2/2
The VPN connection with the sub-network, which is connected to the selected device, shall only allow the use of "CoDeSys" protocol for programming the PLC
  Set the action of the selected policy on „Allow“
  Set the default action on „Deny“
  Mark the check box to not inherit the action from the higher-level folder

## Slide 68: Firewall – Example for inserting the IP filter
Now, the passage of the packages shall be further limited by means of an IP filter  data traffic is only allowed for specific IP addresses
  Adding a rule to the imported policy
  Create a IP filter by input the IP details for this rule
Change of the policy is immediately effective at all folders/devices where it is applied

## Slide 69: Firewall – Example for inserting the user filter
Now, the previously applied filters "protocol" and "IP" shall only become active if the users belong to a certain group  user filter = allocation option in the policy
  Select a device to which the policy should be applied
  Mark the protocol of the policy in the Firewall area and click the button "Edit”
  Select the user or user group from the drop-box and take over these

## Slide 70: Network bridge / Subnetwork
Topic

## Slide 71: Structure sub-network with C6 Router
WAN
RS 232
Server Infrastructure
COMBIVIS connect Control Center
Ethernet
WAN
Bridge with LAN
IP:192.168.210.20
Ethernet
IP:192.168.210.141
IP:192.168.210.142
C6 Router
Local PC
virtual Interface
IP:192.168.210.xxx
IP: 172.17.128.255
COMBIVIS connect Runtime
Notes: Example with connections via Ethernet and serial by using the C6 HMI
In this example we use the C6 HMI as remote device which is connected with the Internet over the Ethernet-Port (LAN2).
A network bridge is created with the Ethernet-Port (LAN1) and one gets a separate sub-network as automation network with the IP address range (e.g. 192.168.210.xxx).
Since two Ethernet ports are available, the Internet access and the sub-network use separated Ethernet ports.
Two F5 devices are connected to the separate sub-network via Ethernet.
In addition, we can see a serial communication between a further F5 inverter and the C6 HMI.

## Slide 72: Internet connection 1/2
Call up and adjust the settings of the Modem connection (Mobile connection)

## Slide 73: Internet connection 2/2
Call up the settings for the network connections
Adjust the Ethernet-Port (WAN) for the Internet access (only, if you don’t use the mobile connection)

## Slide 74: Sub-network (local automation network)
Select the configuration point Ethernet adapter (LAN) to assign the IP address of the sub-network (automation network)

## Slide 75: Structure sub-network with C6 HMI (HMI-Panel)
WAN
RS 232
Server Infrastructure
COMBIVIS connect Control Center
COMBIVIS connect Runtime
Ethernet
LAN2
Bridge with LAN1
IP:192.168.210.20
Ethernet
IP:192.168.210.141
IP:192.168.210.142
C6 HMI
Local PC
virtual Interface
IP:192.168.210.xxx
IP: 172.17.128.255
Notes: Example with connections via Ethernet and serial by using the C6 HMI
In this example we use the C6 HMI as remote device which is connected with the Internet over the Ethernet-Port (LAN2).
A network bridge is created with the Ethernet-Port (LAN1) and one gets a separate sub-network as automation network with the IP address range (e.g. 192.168.210.xxx).
Since two Ethernet ports are available, the Internet access and the sub-network use separated Ethernet ports.
Two F5 devices are connected to the separate sub-network via Ethernet.
In addition, we can see a serial communication between a further F5 inverter and the C6 HMI.

## Slide 76: Network bridge 1/3
Call up the settings for the network connections
Adjust the Ethernet-Port (LAN2) for the Internet access (see the example)

## Slide 77: Network bridge 2/3
Creating a network bridge
Open the COMBIVIS connect Runtime and push the setting icon
Select the Ethernet adapter (LAN1) to bridge this with the virtual adapter
Now, push the button “Create bridge”
After the execution, confirm the message “The bridge has been created”
After reboot, the VPN adapter is currently bridged
Notes: Creating a network bridge in the menue “VPN”
First, you have to open the COMBIVIS connect Runtime.

## Slide 78: Network bridge 3/3
Configure the network bridge settings in the menue “VPN IPs”
Enter and add the IP-address of the network bridge
Push the Button “Apply” to save the IP settings and reboot the C6HMI
After the reboot, you can look at the settings of the network bridge
Notes: Configure the network bridge settings in the menue “VPN IPs”

## Slide 79
Thank you for
your attention!